## Slide 1
Prepared: PE Toan
2026年06月04日
SFG003707 – ICT
Step= 600 Name=D2 Loc=A1 Hi-P= 3 Lo-P= 292 +LM:3.200V -LM:2.700V Act-V= 5.000V Std-V= 3.000V Msr-V= 5.486V Dev=82.86%

## Slide 2
Problem description(5W2H) |  |  | Root cause analysis | 改善對策(Improvement Action)
When: 2026-06-04 | Who: PE Toan | Where: F06 | Defect symptom: Step= 600 Name=D2 Loc=A1 Hi-P= 3 Lo-P= 292 +LM:3.200V -LM:2.700V Act-V= 5.000V Std-V= 3.000V Msr-V= 5.486V Dev=82.86% FA process: Visual check (CCD) shows no abnormality. Retested at ICT station, same failure still occurred Check Log: SMT data review found no abnormal trends, repair history, or test machine concentration. X-ray inspection: No abnormalities detected. Replaced the D2 component and retested ICT; the result passed. Measurement at D2 showed a difference gap between the NG and OK boards. Performed component swap between the OK board and the NG board: Conclusion:Suspected to be caused by NTF. | The issue has been fed back to SPE for further investigation to determine inspection approach and improvement measures. (SPE_Pract – ongoing)
What | SFG003707 ICT Station |  |  | 
Why | Suspected to be caused by NTF. |  |  | 
How | 7pcs * Step= 600 62261161473450 62261161476990 62261161477032 62261161477034 62261161477088 62261161477101 62261161479464 |  |  | 
How Much | DFR: 7/5109 ~ 0.13% (from 00:00 AM-06/03 -> 00:30 AM -06/04) |  |  | 
SFG003707 – ICT – Step= 600 Name=D2 Loc=A1 Hi-P= 3 Lo-P= 292 +LM:3.200V -LM:2.700V Act-V= 5.000V Std-V= 3.000V Msr-V= 5.486V Dev=82.86%
Retest
FAIL
Check
VI_CDD
Measure
Suspected to be caused by NTF
X_Ray
Check
Log
Measurement results from the test station |  | 
Sn | Speck (Ω) | Value (Ω)
62161161181921 | +LM:3.200V -LM:2.700V | 2.886V
62061156710090 | +LM:3.200V -LM:2.700V | 2.939V
62261161473450 | +LM:3.200V -LM:2.700V | 5.491V
62261161477088 | +LM:3.200V -LM:2.700V | 2.680V
62261161477034 | +LM:3.200V -LM:2.700V | 2.680V
62261161477032 | +LM:3.200V -LM:2.700V | 2.676V
62261161476990 | +LM:3.200V -LM:2.700V | 2.686V
62261161477101 | +LM:3.200V -LM:2.700V | 2.685V
62261161479464 | +LM:3.200V -LM:2.700V | 2.675V
Measurements on the PCB |  |  | 
Measurement | PASS | FAIL | 
SN | 62161161180448 | 62261161477034 | 62261161479464
[R] GND → L_P0_TRAFFIC_L | 1.905 MΩ | 1.946 MΩ | 1.889 MΩ
[R] L_P0_TRAFFIC_L → GND | 44 MΩ | 31.47 MΩ | 36 MΩ
[R] GND → 3V3 | 270 Ω | 266 Ω | 271 Ω
[R] 3V3 → GND | 270 Ω | 266 Ω | 271 Ω
[D] GND → L_P0_TRAFFIC_L | 0.880 V | 0.889 V | 0.886 V
[D] L_P0_TRAFFIC_L → GND | OL | OL | OL
[D] GND → 3V3 | 0.211 V | 0.209 V | 0.211 V
[D] 3V3 → GND | 0.211 V | 0.209 V | 0.211 V
Swap component D2 |  |  |  | 
SN | Board Status | D2 Status | ICT Result | Measurement Result
62161161180448 | OK Board | D2 NG | FAIL | 2.682 V
62261161477032 | NG Board | D2 OK | PASS | 2.838 V