## Slide 1
Prepared: PE Toan
2026年06月18日
SFG025080 – ICT
Step=1432 Name=C16 C27 Loc=A1 Hi-P= 12 Lo-P= 1 +LM:40% -LM:40%

## Slide 2
Problem description(5W2H) |  |  | Root cause analysis | 改善對策(Improvement Action)
When: 2026-06-18 | Who: PE Toan | Where: F06 | Defect symptom: Step=1432 Name=C16 C27 Loc=A1 Hi-P= 12 Lo-P= 1 +LM:40% -LM:40% FA process: Visual check (CCD) shows no abnormality. Retested at ICT station, same failure still occurred Check Log: SMT data review found no abnormal trends, repair history, or test machine concentration. X-ray inspection: No abnormalities detected. Measurement at C16 showed no abnormal differences between the NG and OK boards. Conclusion:Suspected to be caused by NTF. | The issue has been fed back to SPE for further investigation to determine inspection approach and improvement measures. (SPE_Pract – ongoing)
What | SFG025080 ICT Station |  |  | 
Why | Suspected to be caused by NTF. |  |  | 
How | 2616V862901904 2616V863437717 2616V863721016 2616V864270202 2616V864286413 |  |  | 
How Much | DFR: 5/4357 ~ 0.11% (from 00:00 AM-06/17 -> 00:30 AM -06/18) |  |  | 
SFG025080 – ICT - Step=1432 Name=C16 C27 Loc=A1 Hi-P= 12 Lo-P= 1 +LM:40% -LM:40%
Retest
FAIL
Check
VI_CDD
Measure
Suspected to be caused by NTF
X_Ray
Check
Log
Measurement results from the test station |  |  | 
SN | Status | Spec (0.820 mF ±40%) | Value (Ω)
2616V862871806 | PASS | 0.492 ~ 1.148 | 1.131mF
2619U1BKC29CKB | PASS | 0.492 ~ 1.148 | 1.125mF
2616V863721016 | FAIL | 0.492 ~ 1.148 | 1.148mF
2616V862901904 | FAIL | 0.492 ~ 1.148 | 1.154mF
2616V864270202 | FAIL | 0.492 ~ 1.148 | 1.152mF
2616V864286413 | FAIL | 0.492 ~ 1.148 | 1.159mF
2616V863437717 | FAIL | 0.492 ~ 1.148 | 1.151mF
Measurements on the PCB |  | 
Measurement | PASS | FAIL
[R] GND → 12V_PCIE(C16) | 2.248KΩ | 2.121KΩ
[R] 12V_PCIE(C16) → GND | 3.07KΩ | 3KΩ
[D] GND → 12V_PCIE(C16) | 0.33V | 0.32V
[D] 12V_PCIE(C16) → GND | 0.38V | 0.38V
SN | MO | MODEL | LINE | GROUP_NAME | IN_STATION_TIME
2616V862901904 | 116736 | SFG025080 | PE | SPI_T | 2026-06-16 02:22:55
2616V863721016 | 116736 | SFG025080 | PE | SPI_T | 2026-06-16 23:59:03
2616V864270202 | 116736 | SFG025080 | PE | SPI_T | 2026-06-17 10:48:34
2616V864286413 | 116736 | SFG025080 | PE | SPI_T | 2026-06-17 10:53:18
2616V863437717 | 116736 | SFG025080 | PE | SPI_T | 2026-06-17 11:40:45